## Slide 1: Accelerometer Controlled Advanced Maze Game Box
Submitted By Project Guide Project Coordinator
-Arun Panwar (Dr.) A. S. Yadav Mrs. Anuradha
-Meghna Goyal Head Of Deptt. Assist. Professor
-Jitendra Sharma E & EE Engg. E & EE Engg.

## Slide 2: CONTENT
Introduction.
Equipments Used in the Project.
Features
Algorithms
Simulation on Proteus ISIS.
Game play and Mazes
Helping Sources

## Slide 3: INTRODUCTION
The main objective is to reinvent the classic “find-your-way-in-the-maze puzzle”.
The ball for which you have to find the way inside the mazes are controlled by the Accelerometer sensor.
It is a collection of Different type of maze games, which includes simple, complex and Dynamic mazes.
The game is displayed using a 128x64 Graphic LCD.
AVR Studio 4 and winavr is used as IDE and Proteus ISIS is used for simulation.

## Slide 4
Equipments Used

## Slide 5
ACCELEROMETER:
ADXL335, 3-axis, +3g and -3g accelerometer is used.
It senses static acceleration of ‘g’ and dynamic acceleration.
It has Five Pin Interface i.e vcc, gnd, x-out, y-out, z-out.
This Accelerometer operates at 3.6 Volt.
Purchased from Robokits.co.in and product code is RKI-1028.

## Slide 6
GRAPHIC LCD:
Graphic LCD “LG128643-SMLYH6V” of Dimension 128x64 is used(ETC Electronic).
It uses KS0108B controller(product of Samsung electronics).
This graphic LCD works on 5 Volt Supply.
It has 20 Pin Interface in which there are 8 data pins and LED+, LED-, Vss, Vdd, Vo, D/I, R/W, E, CS1, CS2, RST, Vee pins are available.
Purchased from robokits.co.in.

## Slide 7
Controller (ATMega 32):
AtMega 32 is a 8 bit product of ATMEL Corp.
It is a 40 pin AVR MCU having 32 kb memory.
It has 4 ports i.e. A, B,C and D.
ADC channels are on the PORT A of this MCU,
so the Accelerometer output pins are at PORT A.
AREF, AVCC and AGND pins are used to set the
reference value, Vcc and GND for ADC.

## Slide 8: Interfacing of Accelerometer
ADC Channel is mounted on PORT A of the ATMega 32, so the Pins of the accelerometer connected to the PORT A.
Signal Conversion by ADC.
For Single ended conversion
Where Vin: the voltage output of Accelerometer
ADC= (Vin*1024)/Vref

## Slide 9: Features of the Games

## Slide 10: Features
Level-1,Level-2 and Level-3 with varying complexity and hurdles.
Interactive GUI and Elemental Features like...
      A Menu For Selecting Different Channels.
      Welcome Screen.
      Rebounding Feature for each Level.
      Dynamic Elements inside levels.
      Score Calculation upto Rank 3.

## Slide 11
      Play, Pause, Reset, Restart and Power ON/OFF Buttons.
      A battery to make game Box Portable.
      A complete Industry ready box setup covering all Equipments under one box i.e. accelerometer, PCB circuits wires etc.
      A handmade charger to charge battery from AC source.

## Slide 12
Game Play and Mazes

## Slide 13
Screenshot of LEVEL-1 Maze, taken from the running Simulation on Proteus ISIS.

## Slide 14
Screenshot of LEVEL-2 Maze, taken from the running Simulation on Proteus ISIS.

## Slide 15
Screenshot of LEVEL-3 Maze, taken from the running Simulation on Proteus ISIS.

## Slide 16: Algorithms

## Slide 17
Algorithm of the Maze Game

## Slide 18
Algorithm of the Maze Game
How Surroundings function works

## Slide 19
Simulation

## Slide 20: Simulation Using Proteus
Simulation is tested using the VSM technology of software “PROTEUS” and its “ISIS Module”.
ISIS (Intelligent Schematic Input System).
Data Pins connected to PORT D of AtMega 32.
Control Pins connected to PORT C of AtMega 32.

## Slide 21
Simulation On Proteus ISIS
A Screen Shot of the Connections Made on Proteus

## Slide 22: Helping Sources
Project using the KS0108B controller library of GLCD
and Font Creator Software,
Produced and Written by- F. Maximilian Thiele, me@apetech.de
Library used for testing on 16x2 LCD is
Produced and Written by- Avinash Gupta, eXtremeElectronics.co.in.
AtMega 32 and GLCD datasheets of ATMEL and ETC INC. respectively.
Google, at each and every step of project.

## Slide 23
THANK YOU
(Any Questions)